## Slide 1: Bi- and Three-dimensional hydrodynamic modeling of the new channel with energy dissipator from the Escuela Colombiana de Ingeniería using ANSYS FLUENT
Jorge Alejandro Mora Uscategui, MSc.,1 Germán Ricardo Santos Granados Ph.D.,2 and Antonio Arenas Amado Ph.D.,3
1 Master of Science Graduate Civil Engineering Department, Escuela Colombiana de Ingeniería; e-mail: alejo.guitar@hotmail.com
2 Professor Civil Engineering Department, Escuela Colombiana de Ingeniería; e-mail: german.santos@escuelaing.edu.co
3 Adjunct Assistant Professor, Department of Civil and Environmental Engineering, Univ. of Iowa,; e-mail: tonoarenas@hotmail.com

## Slide 2: PRESENTATION TOPICS
Methodology
Goals
Future work
Conclusion

## Slide 3: METHODOLOGY
Figure 1. Verification and validation activities and products, for 1D y 3D modeling.
Source. Adapted from (Oberkampf & J. Roy, 2009, p. 30).

## Slide 4: Verification and validation results
  1. Model the free surface of water.
  2. Analyze the dissipation of mechanical energy
  3. Analyze the symmetry of the water:
    Distribution of primary (U) and secondary flows (VW), Cf., Streamlines water.
1. Defining modeling goals
Degree of accuracy required: confidence interval 4% error of measured data.
2. Domain Identification
.
1_Measures in meters.
2_Channel width b = 0.378m
Figure 3. Stability of the flow with and without energy dissipator.
Source. Adapted from (Rodríguez Cárdenas & Camargo, 2013, p. 32-34, 87-88, 107-110)

## Slide 5: Verification and validation results
Topologies proposed for the validation of the channel model ECI No. 2 (channel with 1% slope)
T0_1D
T0_2D
T1_3D
T2_3D
T3_3D
Computational tool used:
Modeling 1D: fourth-order Runge-Kutta method. (Macros – Excel)
2D and 3D modeling: ANSYS FLUENT software.
Hardware: processor Intel® Core™ i7 – 4700HQ CPU @ 2.40GHz - 2.39GHz, 4 Core and 8 Logical processors, 16 GB RAM. Graphic card NVIDIA GEFORCE GTX 760M.
Equation of Reynolds -averaged Navier–Stokes equations > Hypothesis of Boussinesq
Transport equations Turbulence model baseline (BSL) k- w Developed by Menter
Fluid Volume Fraction (Model VOF )
Discretization methods
3. Creating a domain model.

## Slide 6: Verification and validation results
y + = 1 - 10 ... Regions with recirculation with pressure and velocity gradients,
y + = 30 and 500 … Regions where turbulent flow Begins to develop.
Figure 4. Structured mesh used for 2D (a) and hybrid mesh modeling used for 3D (b, c) modeling.
4. Design and creation of the mesh
a)
b)
c)
Geometry
CAD tool
mesh -workbench (2D)
ICEM CFD (3D)
Mesh
square structured cells
Delaunay method (tetrahedron, hexagonal).

## Slide 7: Verification and validation results
Boundary conditions:
The models of multiphase (VOF), of viscosity (turbulence), discretization were configured. Also boundary conditions, relaxation factors for parameters (0.1 for 2D and 0.4 for 3D), residual monitors (10-5, with acceptance criteria 10-3 to 10-5), monitoring surfaces (mass flow and static pressure). Configuring Solution Initialization (initial conditions), autosave and boot (No. Iterations)
4. Design and creation of the mesh (continuation)
5. Configuration of the "Solver" menu of FLUENT

## Slide 8: Verification and validation results
In order to validate the 1D and 3D modeling, a comparison of the measurements in the ECI channel No. 2, with energy dissipator and ramp, of the height of the water surface in the central axis with the models for the flow rate of 18.21 L / s. Measurements were made in the physical model of the height of the free surface of the water in the central axis.
6. Calculation of the solution (Verification of the calculation).
7. Examine the results (Verification of the calculation).
Topology | Number of cells | Computational time (hours) | Iterations
T0 channel long ramp | 104800 | 2.5 | 6000
T1 no dissipater no ramp | 1341579 | 10 | 4350
T2 dissipater and no ramp | 1656589 | 10 | 7000
T3 dissipater and ramp | 1656580 | 10.23 | 7000
Table 5 details the number of cells used for each topology, the computational cost of running the model and the iterations required

## Slide 9: Verification and validation results
Figure 6. Profile water surface measured vs 1D, T3_1D_Q3 (On the central axis).
Profile measured Water surface vs 1D Modeling

## Slide 10: Verification and validation results
Figure 7. Profile Water Surface Measured vs 3D, T3_3D_Q3 (On the central axis).
Profile measured water surface vs 3D modeling

## Slide 11: Comparative modeling
Comparative modeling - 1D vs 2D and 1D vs 3D, water surface depth
(a)
(b)
(c)
(d)
Figure 8. Water profile comparison for Q=18.21 lps and VOF =0.5 (a) 1D and 2D (b) no dissipater and no ramp (c) dissipater and ramp (d) dissipater and ramp

## Slide 12: Comparative modeling
Comparative modeling - mechanical energy
,
Where: : Total mechanical energy or total head. , : Potential or piezometric head. : Head of average kinetic energy, : Head of turbulent kinetic energy. : Lost by friction (Shear stress).
Figure 9. Example of the location of the vertical control sections for the analysis of 2D and 3D scenarios. (In a) Black line = curve of static pressure level. and b): Blue lines = streamline in the direction of flow).
a)
b)

## Slide 13: Comparative modeling
a)
b)
c)
Figure 10. Example of the location of the control sections for the analysis of scenarios with topology T1 (a), T2 (b), T3 (c) in 3D.

## Slide 14: Comparative modeling - mechanical energy
Figure 11. Values of potential energy head hEP (mh2o)
Figure 12. Values of the head of kinetic energy mean hEC (mh2o)
Figure13. Values of friction loss hf (mh2o).
Figure 14. Values of head total energy h (mh2o)
Figure 15. Values of the head of turbulent kinetic energy hk (mh2o)
T1
T2
T3

## Slide 15: Comparative modeling - flow symmetry (distribution of primary and secondary flows)
a)
Figure 16. Primary (U) and secondary (VW), in sections 7 y 8 for topologies T1 (a, b), T2 (c, d) and T3 (e, f).
b)
c)
d)
e)
f)
T1
T2
T3

## Slide 16: Comparative modeling - flow symmetry (Friction coefficient distribution)
Figure 17. Secondary flow influence on the skin friction coefficient distribution in topologies T1 (a, b, g), T2 (c, d, h) and T3 (e, f, i).
a)
b)
c)
d)
e)
f)
g)
h)
i)

## Slide 17: Comparative modeling - Distribution of streamlines
Variable Magnitude velocity, water phase
Streamline from 4 inch pipe alimentation
Figure 18. Streamlines, streaklines and photography for topologies T1 (a). Figure (b) (Rodríguez and Camargo, 2013).
a)
b)

## Slide 18: Comparative modeling - Distribution of streamlines
Variable Magnitude velocity, water phase
Streamline from 4 inch pipe alimentation
Figure 19. Streamlines, streaklines and photography for topologies T2 (a). Figure (b) (Rodríguez and Camargo, 2013).
a)
b)

## Slide 19: Comparative modeling - Distribution of streamlines
Variable Magnitude velocity, water phase
Streamline from 4 inch pipe alimentation
Figure 20. Streamlines, streaklines and photography for topologies T3 (a). Figure (b) present study.
a)
b)

## Slide 20: FUTURE WORK
Implementation of a computer cluster to reduce the computational cost of running the simulations.
Analysis of grid dependency in order to reduce the uncertainty of the results of the simulation.
Transductors and an ultrasound sensor should be installed in the laboratory flume.
Use of apparatus that can measure turbulence are necessary for the calibration of turbulence models
  hot film anemometer (HFA)
  Acoustic Doppler velocimeter (ADV)
  Laser Doppler anemometer (LDA)
  Laser Doppler velocimeter (LDV).

## Slide 21: CONCLUSION
The 1D, 2D and 3D models showed a displacement of the position in which the critical depth occurs in the direction of the flow.
Topology T1 dissipates the energy of the incoming flow given that the ascending flow meets first with dammed water and then with the atmosphere. The flow in this instance continues to be chaotic. By including an energy dissipating transitional structure and a ramp (Topology T3) the flows achieved uniformity sooner.
The turbulent kinetic energy was identified to be responsible for the initial chaotic condition of the flow.
The 3D simulations were used to analyze the symmetry of the flow. Following the results of this analysis future investigations to optimize the transitional structure are encouraged.
According to the results of the work in the laboratory and the 1D, 2D and 3D models, it was found that the use of ramps and structures that reduce the energy of the incoming flow are recommended as they reduce the length it takes the flow to reach uniformity.

## Slide 22: Reference
Nezu, I. (2005). “Open-Channel Flow Turbulence and Its Research Prospect in the 21st Century” Journal of Hydraulic Engineering, ASCE, 229-246.
Andersson, B., Andersson, R., Hakansson, L., Mortensen, M., Sudiyo, R., and Van Wachem, B. (2012). Computational Fluid Dynamics for Engineers, New York, Cambridge University Press.
ANSYS, Inc. (2013). “Ansys help 15.0, Fluent”, Canonsburg, Pensilvania, Estados Unidos.
Bakker, A. (2012). “The Colorful Fluid Mixing Gallery. Obtenido de Course materials for the Computational Fluid Dynamics (ENGS 150)”, Dartmouth College from 2002-2006, <http://www.bakker.org/dartmouth06/engs150/> (Mar. 12, 2015).
Butler, D., & Davies, W. J. (2011). Urban drainage. Abingdon. Taylor & Francis Group.
Cengel, Y. A., and Cimbala, J. M. (2006). Mecánica de fluidos, Fundamentos y aplicaciones, México, D.F., McGraw-Hill/Interamericana Editores, S.A. de C.V.
Chow, V. T. (1994). Hidráulica de canales abiertos, (Juan Saldarriaga, Trads.), Santafé de Bogotá, Mac Graw-Hill Interamericana S.A.
Gautam, B., & Vinayak, E. (2002). Turbulent Flows: Fundamentals, Experiments and Modeling, Kanpur, India, Alpha Science International Ltd.
Mora Uscátegui, J. A. (2017). Modelación hidrodinámica Bi y Tridimensional de dos canales con disipador de energía del laboratorio de la Escuela Colombiana de Ingeniería utilizando ANSYS FLUENT, Escuela colombiana de ingeniería Julio Garavito, Maestría en recursos hidráulicos y medio ambiente, Bogotá.
Rodríguez Cárdenas, H. S., and Camargo, S. A. (2013). Diseño y construcción de un dispositivo de disipación de energía a la entrada del canal experimental de pendiente variable de la ECI, Escuela colombiana de ingeniería Julio Garavito, Especialización en recursos hidráulicos y medio ambiente, Bogotá.
Versteeg, H. K., and Malalasekera, W. (2007). An Introduction to Computational Fluid Dynamics, the finite volume method, Harlow, Pearson Education Limited.