## Slide 2: Forensic engineering and anonymous reporting – Learning from other risky branches of industry
Dr. J.-Martin Hohberg, Berne
Engineers Europe, Swiss NC
1

## Slide 3: My Background
Skills & CPD
EEED Study programmes
EMC EurIng Certificate
BPLC Business Practice
TG Quality (Chair)
E-Learning Board
TG 5.6 BIM Infrastructure
TG 3.5 Forensic Engg.
2

## Slide 4: Your Background
3
What means…
G
A
P
C

## Slide 5: Your Background
4
What means…
G raduate
A ttributes
P rofessional
C ompetencies
&

## Slide 6: GAPC
5
UK Spec:
Management Responsibility
Interpersonal Skills
Professional Attitude
Int. Engg. Alliance (IEA):
Society & Environment
Team Work
Project Management
Lifelong Learning
Engineers Europe

## Slide 7: Civil Engineering as ‘Slow Tech’
6
Slow learning cycle, as deficiency of structures often become only apparent after considerable time due to
slow deterioration processes (e.g. deicing agents unknown in 1960s)
increasing traffic loads and fatigue with time (superseding design criteria)
maintenance requirements sometimes not communicated or neglected
Collapse of Gustav Eiffels’ bridge in Münchenstein 1891 due to increased weight of railway locomotives

## Slide 8: Civil Engineering as ‘Slow Tech’
7
Slow learning cycle, as deficiency of structures become often only apparent after considerable time due to
slow deterioration processes (e.g. deicing agents unknown in 1960s)
increasing traffic loads and fatigue with time (superseding design criteria)
maintenance requirements sometimes not communicated or neglected
Collapse of Morandi’s Polcevera viaduct in Genova 2018 due to corroded cable-stays (difficult to inspect)

## Slide 9: Overstretching Known Application Boundaries
8
Sudden collapse early in the life cycle, during construction or commissioning, may occur because of
insufficient consideration of temporary construction stages
unknown safety margin or unfamiliar instability modes
additional complications hitherto unknown or neglected in design
Collapse of the Malpasset Dam in Frejus 1959 due to shearing off of left abutment under uplift in the rock

## Slide 10: Overstretching Known Application Boundaries
9
Sudden collapse early in the life cycle, during construction or commissioning, may occur because of
insufficient consideration of temporary construction stages
unknown safety margin or unfamiliar instability modes
additional complications hitherto unknown or neglected in design
Collapse of the Florida FIU Pedestrian Bridge 2018 during erection of precast span (design intent not understood)

## Slide 11: Benefits of Forensic Engineering
10
Often collapses, for instance during structural alteration, originate not from a single large defect, but a combination of hidden flaws. Active and latent failure in different barriers of resistance may contribute.
Identifying such repeatingly found shortcomings and vulnerable details results in recognizing patterns of design issues to improve – beyond the individual unique structure.
Swiss cheese model as used in healthcare

## Slide 12: Shortcomings of Forensic Engineering
11
Concentration on finding the technical reason for the structural malbehaviour, develloping investigation methods.
Unfavourable non-technical circumstances are considered beyond the technical scope and left to court experts.
Ishikawa or fishbone diagram in manufacturing
material
machine
method
man
management
milieu
‘6 M’

## Slide 13: Shortcomings of Forensic Engineering
12
Concentration on finding the technical reason for the structural malbehaviour, develloping investigation methods.
Unfavourable non-technical circumstances are considered beyond the technical scope and left to court experts.
‘Environment‘ not to be limited to physical climate!
Ishikawa or fishbone diagram in engineering
design
equipment
procedure
operator
supplies/material
environment
‘DISPOSE’

## Slide 14: Swiss Transportation Safety Investigation Board
13
Meticulous reconstruction of the course of event, including subjective beliefs of persons involved; looking also for «accepted wrong behaviour» in the working environment (incl. hierachical intimidation and group think)
e.g. red signal light violation:
why did the driver expect green signal light?
was the signal not clearly visible? Etc.

## Slide 15: Swiss Medical CIRS System
14
CIRS = Critical Incident Report System
with the aim of vigilance against unex-pected problems with medication or complications occurring in hospital
Issuing of "Quick-Alerts", e.g. No. 50: Wrong setting of medical devices like dosing pumps (collection of several similar cases)

## Slide 16: CROSS-UK for Buildings
15
CROSS = Collaborative Reporting for Safer Structures
Grenfell Tower 2017

## Slide 17: e-Learning as CPD Tool
16
IABSE webinar May 2021
IABSE - Webinars

## Slide 18: 5 Corollaries for Engineering Education
17
Raise awareness by teaching Engineering History in the very first semester.
Don’t just portrait acclaimed design heros, but team efforts in their design studios; thereby focus also on robustness and life-cycle thinking.
Invite paractisioners to talk about surprises, pitfalls and solutions in their designs; Contractors about buildability; and owners of structures about maintenance and latent defects.
Risk management, Peer Review and ‘post-mortem’ analysis must become integral part of the engineering culture.
Offer Decision Theory and Systems Engineering as eligible master courses.

## Slide 19: Take away
18
Sources of uncertainty:
From unknown Knowns…
…to known Unknowns…
…and unknown Unknowns.
Note: There are many uncertains in engineering, not all matter. Risks are uncertainties that do matter.
(after David Hilson)